## Slide 1
What is MES?
Manufacturing Execution System — the essentials, before we review the project
In one line: software that runs the shop floor in real time — it tells each operator exactly what to do, stops them doing it wrong, and records what actually happened.
How it fits together
ERP
Plans the work What to make, how much, by when — orders, BOM and material master.
MES
Runs and proves the work Guides the operator, validates every material and lot, records what actually happened.
PLC / SCADA
Does the work Feeders, mixers, scanners and printers physically executing on the floor.
▼ orders, BOM, material master ▲ consumption, production confirmation
▼ instructions, interlocks ▲ signals, tags, actual events
What MES does, every shift
1
Identify Every lot gets a QR code the moment it is booked in.
2
Guide Tells the operator which material, which feeder, how much.
3
Prevent Blocks the wrong material before it enters the mix, and locks the machine.
4
Record Links every batch back to the exact input lots that made it.
Why it matters to the business
Quality
Wrong material is stopped at the feeder, not discovered later in the lab.
Traceability
Full batch genealogy in seconds — a recall narrows from a month of output to one lot.
Cost
Actual consumption measured against BOM, making give-away and losses visible.
Compliance
An audit trail captured automatically as work happens, not reconstructed later.
MES is not ERP (it does not plan) and not SCADA (it does not control machines) — it is the layer in between.
Our scope: 33 stations across 8 areas,
RMS booking through to mixer batch off.
Notes: Purpose: give the CEO a working mental model of MES before the project review. 1. Definition — MES runs the shop floor in real time. 2. The stack — ERP plans, MES executes and proves, PLC/SCADA physically acts. MES is the translation layer; data flows down as instructions and back up as confirmed reality. 3. Four verbs — Identify, Guide, Prevent, Record. 'Prevent' is the one that changes behaviour on the floor (poka-yoke). 4. Business case — quality at source, traceability for recall, cost visibility against BOM, automatic audit trail. 5. Boundary — MES is not ERP and not SCADA. Expect this question.