## Slide 1
TECHNICAL WALKTHROUGH
MES IMPLEMENTATION | GATES INDIA LALRU

## Slide 2: agenda
1. Plant Study Report
2. Proposed Solutions
Smart MES Solution

## Slide 3: No of machines or stations
Serial No | Area | No of Machines | Description
1 | RMS Booking | 1 | Raw material storage, receipt, and placement in the storage area.
2 | RMS Issue | 2 | Issue material to shop floor from raw material storage.
3 | Carbon Silica & Other | 12 | 12 feeders feed material.
4 | Oil | 10 | Oil stations for specific materials.
5 | Auto Chemical | 2 | Approx. 50 bins for feeding in each small chemicals.
6 | Bale Cutter | 2 | Cutting polymer into separate lots.
7 | Mixer Feeding | 2 | Operator feeds polymer/compound based on recipe.
8 | Mixer Batchoff | 2 | Load batch output onto skid.
Total | Total | 33 | 

## Slide 4: RMS Requirement
GRN Booked in ERP System.
ERP system will send data to MES.
MES will have option to split material quantity into sub lots.
MES will have Option to print QR code and sticker.
MES will have option to select storage location.
In case GRN is cancelled or Quality is changing ERP will share the information with MES.
MES will maintain RMS inventory material wise location wise and aging wise.
1 PC for MES client, Where user can open the MES for access GRN data and give print command.
2 Printer one is for sticker and another one is for tag.
LAN Network is required to connect these PC and Printers with MES server.
RM Booking Requirement
RM Booking Required hardware

## Slide 5: RMS Requirement
User will create Issue slip based on PPC Requirement.
Based on issue slip, user issues the material with MES System.
On material Issue System will Validate material, quantity, aging, and FIFO.
After material Issue completed based on Issue slip.
MES will have option to complete the Issue slip.
On Issue slip complete MES will Update the inventory.
MES will share data with ERP also.
2 Wi-Fi Mobile scanner required.
Issue slip user can generate in RMS PC.
Wi-Fi Network is required in RMS Store.
RM Issue Requirement
RM Issue Required hardware

## Slide 6: Carbon Silica & Other Feeders Requirement
Material wise feeder lookup will be required to validate the material..
On wrong material scanned Crane should not run.
Andon light should indicate on wrong or right material scan .
Crane control system and Andon light PLC integration.
Feeders will be identified with metal barcodes.
2 Bluetooth wireless scanners required.
12 Andon lights.
One HMI to display feeder wise material lookup.
12 Metal barcode for each feeder.
Network connectivity for all devices.
Andon lights connectivity with PLC
Feeders Requirement
Feeder Required hardware

## Slide 7: OIL Feeders Requirement
Material wise oil feeder lookup will be required to validate the material..
On wrong material scanned door should not open.
Andon light should indicate on wrong or right material scan .
Door open control system and Andon light PLC integration.
Oil Feeders will be identified with metal barcodes.
2 Bluetooth wireless scanners required.
10 Andon lights.
One HMI to display feeder wise material lookup.
10 Metal barcode for each feeder.
Network connectivity for all devices.
Andon lights connectivity with existing PLC
OIL Feeders Requirement
OIL Feeder Required hardware

## Slide 8: Auto chemical Requirement
Material wise bin lookup will be required to validate the material..
On wrong material scanned bin door should not open.
WinCC Flexible SCADA is in place which is logging material and bin wise consumption.
PLC or Scada has information about what production is planned , running and completed.
Each trolly will be identified with unique barcode.
One MES HMI display to display trolly status , bin lookup and running and production history.
Produced bags will be liked with input material.
With trolly scan in mixing area bag consumption will be linked with batch id.
2 Wi-Fi mobile scanner for loading bins.
2 Bluetooth wireless scanners required.
2 HMI to display .
Network connectivity for all devices.
auto chemical Requirement
Auto chemical Required hardware

## Slide 9: Bale Cutter Requirement
Bale cutters 2 different lots material can be mixed in one lot.
After bale cutter final unique lot no will be generated and linked with source lot to trace the material.
2 Printers.
2 USB scanners required.
2 HMI to display .
Network connectivity for all devices.
Bale Cutter Requirement
Bale Cutter Required hardware

## Slide 10: Mixer Feeding Requirement
Mixer feeding area MES will monitor running material production plan and recipe.
Based on the same BOM will be displayed to check material validation status.
Before weighing user will scan polymer or compound.
Conveyor will run in case of right material scanned and validated.
Carbon and others material directly consumed from bins.
All the input material will be linked with produced batchID.
Mixer control system PLC tags will have running production detail like plan id , recipe and material code.
2 HMI display .
2 Wi- Fi Scanners.
Network connectivity for all devices.
Mixer Feeding Requirement
Mixer Feeding Required hardware

## Slide 11: Mixer Batch Off Requirement
Mixer Batch area MES will monitor batch off start and stop.
On batch off stop user will enter no of batch taken out.
MES is already tracking batched in FIFO from mixer production.
MES will print the stickers for the batches taken out.
2 HMI display .
2 printers
Network connectivity for all devices.
Mixer Batch Off Requirement
Mixer Batch Off Required hardware

## Slide 12: PROJECT ASSUMPTIONS

## Slide 13: Implementation roadmap
Phase wise implementation
Overall system design and data flow architecture.
Central MES System hosted at Common On-Premise Data Center.
Integration of mixing area for traceability and execution control.
MES for traceability and controls.
  RMS Booking
  RMS Issue
  Carbon Silica & Other (Poka Yoke)
  Auto chemical.
  Mixer Feeding (Poke Yoke)
  Mixer batch off.
Phase Wise Delivery | Total Requirements
Phase 1 | 8
Grand Total | 8
Questionnaire :
Phase 1

## Slide 14: SCOPE OF WORK
Phase 1 - mes
Master Data Management
Work Order Execution
Material management
BoM Management
User Management
Tag printing
MHE mapping
Production & consumption
Quality Control
System Integrations
Oracle ERP
Warehouse
Reports
RMS Integration
Production , consumption report
Traceability report
Shopfloor material movement
2. Scada , PLC
Error proofing & material validation
Material Aging and FIFO control

## Slide 15: Smart MES Architecture
SCADA
PLC
Item Management
Smart Integrator
MES Application
MES Database
Data Warehouse
Smart Reports
MES Server
Machines
On Premise
Shopfloor
MES Client
Shopfloor
MES

## Slide 16: Proposed solutions
Smart MES Portfolio
Tailoring Smart MES solution to provide single solution catering all the requirement.
1
MES
2

## Slide 17: implementation Basis
Implementation stages
MS No | Milestone Name | Key Activities | Deliverables
1 | Requirement Freeze & Workshop | Plant visits & process understanding. Requirement gathering workshops. | BRD Signoff
2 | Functional Design Session | Functional Design Documentation Interface Control Design Documentation | FDS Signoff ICD Signoff To-be UAC
3 | Solution Build & SIT | Build & Developments Unit Testing & UAC testing SIT Deployment | UAC Signoff Solution Demo
4 | User Acceptance Testing | UAT Deployment Solution test and acceptance test. Key User Training | UAT signoff
5 | Commissioning & Go Live | Production Deployment | Go Live Acceptance Document
6 | Roll Out | Handover training Training videos | Handover Training Training Videos

## Slide 18: PROJECT EXCLUSIONS
Hardware & third-party Software supply is not included in current proposal
No IT infrastructure and networking analysis is included in the current proposal.
No legacy data will be migrated to MES during the project
Materials and activities on field devices and equipment (e.g., PLCs modification). Or modification of existing equipment for any process automation.
Providing and Coordinating warranty support for hardware, DB, OS, Hypervisor, SCADA, PLC or any third-party software / application.
No Hardware mounting & network configuration considered in current scope

## Slide 19: GENERAL ASSUMPTIONS
The language for project, training, operator’s documentation will be english.
Services will be conducted onsite or off-shore basis as needed.
System maintenance: customer's it will perform regular backups and restoration of the whole system, databases.
Any scope changes agreed with customer will be taken up separately through a change request (cr) mechanism.
Any delay in response due to non-availability of the external system, support personnel or due to development of additional interfaces / features / bug-fixes by external parties, will impact the project schedule and hence the cost consequently.
Final production deployment architecture/recommendation and sizing will be reevaluated during project definition phase.
Customer is responsible to perform system validation, including developing and executing test cases (user acceptance test) to validate requirements and system functionality. SCIL will respond to issues and concerns raised during the validation stage.

## Slide 20
Thank you